## Slide 1: Solar Monitoring Panel BTech 451 Final Seminar
David Armstrong – 5636534
Academic Supervisor: Ulrich Speidel
This project is with Vector Limited

## Slide 2: Background – Vector Limited
Vector Limited
  Auckland-based
  Primary a power distribution company
  Gas
  Fibre
Recently begun to investigate a solar optimisation challenge that the global solar industry is facing
  As with other distribution networks

## Slide 3: Research Question
The research question: “Can the strategic use of excess power provide additional value to the customer?”
  The goal of the project is to answer this question
  To answer the question, I will produce a load-switching solution
Question is based on optimising the use of excess power to provide additional value
Example situation with optimisation potential:
  Exporting power when reimbursement rate is low

## Slide 4: Background – Solar Panel System
Solar panels on the roof generate power
Power can be stored in onsite battery for later use
  Can be used overnight or during power cuts
Excess power can be exported to the grid
  Reimbursed at different rates
System is connected to internet via home internet connection
Has an HTTPS-based API
  Can retrieve system status and power plan information in XML or JSON formats

## Slide 5: Background – Logical Diagram

## Slide 6: Solution Design
Hardware component
  A cheap, low-powered device running in the house
  Needs to support an appropriate programming language
  Switch both wireless and/or wired loads
Software component
  Program that loops indefinitely
  Retrieve system status using the HTTPS-based API
  Make decisions based on status and recent history each loop iteration
  Send control signal to switches

## Slide 7: Solution Design - Choices
Device - Need a cheap but reasonably powerful device to connect using API, make decisions and send control signals
  Arduino
  Raspberry Pi
Programming Language – Needs to be to run for a long time and have HTTPS and GPIO libraries
  Python
  Java
  C++

## Slide 8: Solution Design– Logical Diagram

## Slide 9: First Semester Progress
Understanding of the system and API
Raspberry Pi configuration
  Got Java programs to run
Decision Making Program
  Functional – Program structure works
  API Methods working correctly
  GPIO control signal tested and working with a LED
  Lacks intelligent decision-making logic

## Slide 10: Second Semester Progress
Decision making logic algorithms
  Iterative process – several versions
  Store recent information, in memory and in CSV files
  Use this recent information to help make decisions
Controlling multiple loads
  Updated GPIO controller to switch additional loads
  Decision logic takes multiple loads into account
  Loads have priorities
php parameter editor
  Change load information via web (local network)

## Slide 11: Decision Making Algorithms
1st Algorithm
  4 Basic conditions based on information such as:
    Amount of power currently being exported
    How much power has been exported recently
  Designed for a single load
  Found it didn’t turn on loads enough
2nd Algorithm
  Based on the first algorithm but with state machine simulations
  Designed for a single load
  Found it was too hard to simulate systems

## Slide 12: Decision Making Algorithms
3rd Algorithm
  Based on the first algorithm, but with a few changes
  Designed for a single load
  Better than the first, but still didn’t turn loads on enough
4th Algorithm
  The most simple, but also the most effective
  Designed for multiple loads
  Turns on loads effectively

## Slide 13: Implementation- Classes
DecisionMaker.java
  Contains the main method, initiates the program
  Contains decision making logic
APIConnection.java
  Contains methods for using the API, like getting current status
Logger.java
  Contains static methods for logging to CSV files
LoadController.java
  Contains methods for controlling GPIO

## Slide 14: Implementation- Classes
DayData.java
  Stores data in memory for a particular day
  Statistic info is generated at the end of the day
DataRecord.java
  Stores multiple DayData objects in memory
  Calculates information from multiple days to be used for decision making
SystemStatus.java
  Basic data class that holds information about a system

## Slide 15: Implementation Summary
Program consists of 7 Java classes
The program runs successfully on the device and loops indefinitely
At each iteration of the loop, the device successfully turns multiple loads on or off depending on:
  The current state and recent history of the system
  Priority of the loads
Loads only turn on during power export
Loads are switched either by a wired switch, or remote switches

## Slide 16: Live Demo

## Slide 17: Answer to the Research Question
The research question: “Can the strategic use of excess power provide additional value to the customer?”
Answer: Yes, if the loads being turned on are useful and don’t just waste power
  No point turning on a load just to waste it
  Loads should consume excess power in a useful way that can provide additional value, e.g. Hot-water preheater

## Slide 18: Potential future work
Test more thoroughly
Look at longer term effects/trends
Display statistical information to the user
  Web interface
  Smartphone app
Alert users when excess power is available
  Instead of switching on loads automatically
  Send user an email
  App notification on local network (if home)

## Slide 19: What I have gained
Long term project experience
  Time management
Enhanced Java and OOP skills
Basic php experience
Written communication skills
  From reports, documentation and emails
Verbal communication skills
  From presentations and meetings
Business experience

## Slide 20: Thank you, any questions?