## Slide 1: Solar Monitoring Panel BTech 451 Mid-Year Seminar
David Armstrong – 5636534
Academic Supervisor: Ulrich Speidel
This project is with Vector Limited

## Slide 2: Background – Vector Limited
Vector Limited
  Auckland-based
  Primary a power distribution company
  Gas
  Fibre
Recently begun to investigate a solar optimisation challenge
  As with other distribution networks

## Slide 3: Background – Solar Panel System
Solar panels on the roof generate power
Power can be stored in onsite battery for later use
  Can be used overnight or during power cuts
Excess power can be exported to the grid
Components are connected together by an onsite computer
Connected to the internet via home internet connection
  Can be remotely controlled

## Slide 4: Background – Logical Diagram

## Slide 5: Background - API
HTTPS based
  GET, POST, DELETE methods
Features
  Initiate / end session
  Get current system status in XML/JSON format
  View/modify power plans
Newer version of API was released recently
  Better features
  Had to rewrite API code

## Slide 6: Research Question
Assigned to me by Vector for me to work on
Based on a current challenge that the global solar industry is facing
Situations of power use where there is optimisation potential
  Exporting power when reimbursement rate is low
  Exporting early then importing to later power a device
The research question: “Can the strategic use of excess power provide additional value to the customer?”

## Slide 7: Solution and Answer
Have an optional load in the house turn on to consume the excess power
  Decision is made on current system status and recent history
  Load would be switched on automatically
  Could potentially alert user to turn a load on manually
Use a local device in the house to this
  Connect using API
  Make decisions
  Send control signal
Answer the research question based on this solution

## Slide 8: Solution – Logical Diagram

## Slide 9: Technical Choices
Device - Need a cheap but reasonably powerful device to connect using API, make decisions and send control signal (GPIO)
  Arduino
  Raspberry Pi
Operating System – Need a Stable OS for the Raspberry Pi that supports modern programming languages
  Raspbian
  Pidora
  Arch Linux

## Slide 10: Technical Choices
Programming Language – Needs to be to run for a long time and have HTTPS and GPIO libraries
  Python
  Java
  C++
Status return format – Needs to use low bandwidth
  XML
  JSON

## Slide 11: Current Progress - Overview
Raspberry Pi configuration
Decision Making Program
  Functional – Program structure works
  Lacks intelligent decision-making logic
  API Methods
  GPIO control signal tested and working with a LED, but not connected to a relay yet

## Slide 12: Current Progress - Classes
DecisionMaker.java
  Contains the main method, initiates the program
APIConnection.java
  Contains methods for using the API, like getting current status
LoopTask.java
  Contains high-level logic , Subclass of Thread
Logger.java
  Wrapper methods for logging
LoadController.java
  Wrapper methods for controlling GPIO

## Slide 13: Live Demo

## Slide 14: Future Work
Improve decision-making algorithm logic
  Record recent history on the device
  Compare the current day to recent history
  Estimate the remaining power to be generated this current day
  Make a decision accordingly
Setup up the Raspberry Pi in a box with a relay
  Set up Raspberry Pi in a circuit with a relay to turn load on/off
Feed decision information back to Vector

## Slide 15: Thank you, any questions?