## Slide 1: Welcome to COMPSCI111/111G
Summer School 2016

## Slide 2: Today’s class
Introduction to COMPSCI111/111G
  People
  Assessment
  Labs
  Test and exam
Introduction to hardware
Bits, bytes and digital information

## Slide 3: Lecturers
Damir Azhar
  damir.azhar@auckland.ac.nz
  303S, Level 3, room 390
Reuel Baptista
  reuel.baptista@auckland.ac.nz
  303S, Level 5, room 567
Paul Ralph
  p.ralph@auckland.ac.nz
  303S, Level 4, room 492
We all have an open door policy. Visit anytime or email for an appointment

## Slide 4: Course coordinator and lab supervisor
Ann Cameron
  303S, Level 4, room 479
  a.cameron@auckland.ac.nz
  Open door policy. Visit anytime or email for appointment
Contact Ann if you have questions about the course or labs

## Slide 5: Computer Science Support Network
Radu Nicolescu
303-587 Ext: 86831
E-mail: r.nicolescu@auckland.ac.nz
Ann Cameron
Room: 303S.479
Ext: 84947
E-mail: ann@cs.auckland.ac.nz
Angela Chang
Room 494
Ext: 86620
Email: angela@cs.auckland.ac.nz
Pat Riddle
Room: 303S.392
Ext: 87093
Email: pat@cs.auckland.ac.nz
Andrew Luxton-Reilly.
Room: 303S.479
Ext: 85654
Email: andrew@cs.auckland.ac.nz
Paul Denny
Room: 303S.465
Ext: 87087
Email: paul@cs.auckland.ac.nz
Adriana Ferraro
Room: 303S.490
Ext: 87113
Email: adriana@cs.auckland.ac.nz
Need to talk to someone?
We are here to
listen and help!
Come and talk to us!

## Slide 6: Marks for COMPSCI111/111G
Theory: exam and test
Practical: labs
Need to pass half of the theory and half of the practical in order to pass the course
Exam (60%)
Test (20%)
Labs (20%)

## Slide 7: Test
Wednesday 27 January, 11.30am-12.30pm F&PA Auditorium
The test will cover lectures 1-14 and labs 1-5

## Slide 8: Labs
An opportunity to practise what you learn in lectures
  2 compulsory 3-hour labs each week
  9 labs worth 20% of final mark
  10% of each lab’s mark is given for arriving on time
  Hand in lab assignment before start of next lab
Before labs start on Thursday please:
  Buy a lab manual from UBS
  Find the First Floor Teaching Lab (FTL - 303S-175)
  Make sure you have a USB drive

## Slide 9: Exam
Date and location will be announced by the Exams Office

## Slide 10: Class representative

## Slide 11: Places to find information
Canvas and email announcements
The course website: www.cs.auckland.ac.nz/courses/compsci111ssc
You need to purchase a 2016 Summer School lab manual from UBS
Coursebook; available on the home page of the course website
The Computer Science student forum: http://forums.cs.auckland.ac.nz
Any of the COMPSCI111/111G teaching staff 
  Please use your University email account when emailing us

## Slide 12: Computer Hardware
Lecture 1 – COMPSCI111/111G SS 2016

## Slide 13: Today’s lecture
Identifying the key components in a computer
Understanding how these components work
Using this knowledge to understand computer specs

## Slide 14: Overview of a computer
Input
Processing
Storage
Output
Communication

## Slide 15: Computer hardware
“Those parts of the system that you can hit with a hammer (not advised) are called hardware”
Key design principle of modularity
Monitor
Keyboard
Mouse
System Unit

## Slide 16: Form factors
System units come in lots of different form factors
All-in-one PC

## Slide 17: Inside the system unit
Power supply
Fans
CPU
Expansion cards
Hard disk drive
Optical drive
RAM
Motherboard

## Slide 18: Inside a laptop
Power supply (batteries)
Fans
CPU
Optical drive
RAM
Motherboard
Hard disk drive

## Slide 19: Power supply unit
Converts AC voltage to DC voltage for use within the computer

## Slide 20: Motherboard
The main circuit board to which all components are connected, allowing them to communicate with each other

## Slide 21: Central processing unit (CPU)
The ‘brain’ of a computer. Processes data in a computer using its instruction set
Performance measured in instructions per second
Clock speed (measured in Hertz [Hz]) measures the speed at which electrical signals pass through the processor
CPUs must be kept cool, generally using a heatsink and fan

## Slide 22: CPUs - transistors

## Slide 23: CPUs – Moore’s Law
Gordon Moore (Intel co-founder) stated in a 1965 paper: ‘The number of transistors on a single integrated circuit doubles approximately every 18 months, while the price remains the same.’
So…
  In 3 years, CPUs will be 4 times faster
  In 15 years, CPUs will be 1000 times faster

## Slide 24: CPUs - Moore’s Law
Moore’s Law has been an important guide for many aspects of the tech industry, especially in CPU manufacture
We’re finding it more difficult to keep up with Moore’s Law as we reach the limits of our fabrication technology

## Slide 25: CPUs – other measures
Power efficiency and heat are just as important as clock speed
Modern CPUs have multiple cores, increasing their processing capacity
New kinds of processors, such as system on chip (SoC) are commonly used in mobile and embedded devices

## Slide 26: Wirth’s Law
Niklaus Wirth stated in 1995 that ‘software gets slower more rapidly than hardware gets faster’

## Slide 27: Primary memory
Used to store data for quick access by CPU
Main form of primary memory is Random Access Memory (RAM)
RAM is volatile memory
More RAM improves a computer’s speed by providing more quick access memory
Capacity is measured in bytes, clock speed measured in Hz
Many types of RAM; common type is DDR3 SDRAM

## Slide 28: Secondary memory
Used to store files for repeated access over time
Also known as non-volatile storage; the storage medium retains its contents without electricity
Many forms of secondary storage:
  Hard disk drive (HDD)
  Solid state drive (SSD)
  CDs, DVDs, Blu-ray
  USB drives, external HDDs

## Slide 29: Hard Disk Drive (HDD)
Stores data on spinning magnetic disks. Data is read and written by moving heads
Advantages:
  Cheap storage medium
  Widely used and supported
  Can have very large capacity drives
  Long operating life
Disadvantages:
  Noisy operation
  Can consume more power than SSDs
  Fragile, needs to be handled carefully

## Slide 30: Solid State Drive (SSD)
Stores data on flash memory, the same technology used by USB drives
Advantages:
  Silent operation
  Higher read/write rates when compared to HDDs
  Low power usage
  More durable
  Use less space
Disadvantages:
  Costlier than HDDs
  Can wear out faster than HDDs

## Slide 31: Memory capacity

## Slide 32: Expansion cards
Additional circuit board that provides extra functionality
Examples: sound card, graphics card, network card
Plugged into motherboard using slots that follow certain standards:
  ISA
  PCI-E
  AGP

## Slide 33: Graphics card
Used to perform graphics processing and run the computer’s monitors
Consists of:
  GPU (built-in/discrete)
  Video memory
  Heatsink and fan
  Ports

## Slide 34: Redundant Array of Independent Disks (RAID)
RAID pools HDDs/SSDs together to form a larger, more reliable data storage mechanism
Each RAID configuration has its own strengths and drawbacks
RAID is commonly used in servers
Data
RAID
Controller
Hard Disk 01
Hard Disk 02
Hard Disk 03

## Slide 35: RAID configurations
Numerous configurations, we’re focusing on two:
  RAID 0 – data stripes used to increase speed
  RAID 1 – data redundancy used to increase reliability
RAID 10 combines RAID 0 and RAID 1 together
RAID 10

## Slide 36: Input devices
Peripherals that enables the user to provide information to the computer
Common input devices:
  Keyboard
  Mouse
  Webcam
Other input devices:
  Voice recognition
  Biometric scanners
  RFID tags

## Slide 37: Output devices
Peripherals that present information processed by the computer to the user
Output devices include:
  Computer monitor
  Printer
  Speakers
  Touchscreens
New forms of output include:
  Virtual reality

## Slide 38: Connectors and buses
All peripherals are connected to the motherboard via ports
Ports form part of a bus
Wired connections:
  USB (Universal Serial Bus)
  Firewire and Thunderbolt high speed buses
  Ethernet
  VGA, DVI and HDMI for monitors
Wireless connections:
  Wi-Fi
  Bluetooth

## Slide 39: Computer specs
How much primary memory does this computer have?
How many cores does the processor have?
Does this computer have a motherboard?
Does this computer have a graphics card?

## Slide 40: Summary
Computers process input from the user and other sources and provide output
Computer systems are designed using the principle of modularity
System units are made up of a number of components working together:
  Power supply
  Motherboard
  CPU
  Primary and secondary memory
  Connectors and buses