## Slide 1: More on Assembly
CS 210 Tutorial 5
Assignment preparation

## Slide 2: Difference between ldiq and ldq
Ldiq is for loading immediate value into register
Ldiq $t0, 0x8000;
Ldq is for reading memory in specific location
For example: Memory has values
0x8000 : 0x1111111111111111
0x8004 : 0x2222222222222222
Ldq $t1, ($t0); value in $t1 is 0x1111111111111111
Ldq $t1, 8($t0); value in $t1 is 0x2222222222222222

## Slide 3: getChar
Take char value from keyboard to $v0

## Slide 4: PutChar
Take char from $a1 put to screen

## Slide 5: Printout example
block main uses proc, CALLSYS {
data {
align;
buffer:
asciiz “tide";
} data
code {
public enter:
ldiq $s0, buffer;
{
while:
ldbu $a1, ($s0);
beq $a1, end;
do:
ldiq $a0, CALLSYS_PUTCHAR;
call_pal CALL_PAL_CALLSYS;
addq $s0, 1;
br while;
end:
}
clr $a0;
bsr Sys.exit.enter;
} code
} block main

## Slide 6: Exercise – checking blocks

## Slide 7: Result – checking blocks

## Slide 8: Read keys and store in memory
code {
public enter:
ldiq $t6, 0x01ffe184;//for example using hardcode
{
loop:
ldiq $a0, CALLSYS_GETCHAR;
call_pal CALL_PAL_CALLSYS;
//blt $v0, end;
mov $v0, $a1;
mov $v0, $t5;
stb $t5, ($t6);
addq $t6, 1;
ldiq $a0, CALLSYS_PUTCHAR;
call_pal CALL_PAL_CALLSYS;
br loop;
end:
}
{
clr $a1;
ldiq $a0, CALLSYS_EXIT;
call_pal CALL_PAL_CALLSYS;
}
} code

## Slide 9: Reverse example
Check the code and try to understand it.
Match them together to finish assignment.