## Slide 1: CA406
Computer Architecture
Experimental Design

## Slide 2: Experimental Design
Good design
  Saves Time
  Gets better results!
Hypothesis - essential starting point
  Form one before doing the experiment
  Use theory to predict results
    Examples
      Time for this program will be proportional to the size of the problem
        O (n) running time

## Slide 3: Theoretical Prediction
Example
Time is linear in size of problem
Time
(sec)
Size of problem - n
Time
Complexity
O(n)

## Slide 4: Theoretical Prediction
but ...
Time will increase sharply when cache is full
Time
(sec)
Size of problem - n
Cache
overflows
Data fits
in cache
Running time jumps!

## Slide 5: Refine the prediction!
Time will increase sharply when cache is full
How sharply?
Time
(sec)
Size of problem - n
Cache
overflows
Data fits
in cache
More likely!
You can probably
estimate the shape of
this curve

## Slide 6: Why not just do some measurements?
Experiments are always subject to errors
Time
(sec)
Size of problem - n
Cache
overflows
Data fits
in cache
Expectation
Sharp jump here
Experiment
Measure up to here

## Slide 7: Why not just do some measurements?
Cache
overflows
Data fits
in cache
Experiments are always subject to errors
Time
(sec)
Size of problem - n
No clear trend,
so fit a straight line
Actual measurements
No sharp
jump?
 No cache!

## Slide 8: Why not just do some measurements?
Measure up to here
Make sure to carry the experiment far enough!
Time
(sec)
Size of problem - n
Cache
overflows
Data fits
in cache
No sharp jump
but sharp increase
in slope
as predicted!
but ..
Measure as far as here
and it’s clear!

## Slide 9: Cache Problem
L1 Cache Size
Real Shape!
From simple model

## Slide 10: Errors
Random errors
  Repeat a measurement
    Deviations from mean are random errors
    Limited clock resolution can produce these
dt = 0.8*(timer resolution) randomly reported as 0 or 1

## Slide 11: Errors
Systematic errors
  Results are perturbed in one direction
    OS will interrupt
    All times are lengthened
Error Reduction
  Reduce quantisation effects
    Ensure dt >> timer resolution
  Make several measurements
    Use minimum?
      Still likely to have OS contribution!
    Use mean?
      Includes average amount of OS overhead

## Slide 12: Generating conclusions
Estimate errors first
  Add error bars before fitting curves
  Same data - different errors
Only a curve fits!
A linear relation is possible!

## Slide 13: Generating conclusions
If your original hypothesis suggested a linear relation, failure to adequately allow for error would have sent you off on a fruitless search for a new hypothesis!
Only a curve fits!
A linear relation is possible!

## Slide 14: Transform Data
Use your hypothesis
  Usually transform data to linear form
  O(n2) algorithm
  Running time for problem size n,
    t(n) = c n2
  Divide experimental times, t(n) by n2
    constant, c
  Use the computer to generate a table of normalised data
    It’s very good at these simple, boring tasks!
    It’ll also print out a neat table for your report!

## Slide 15: Presenting data
Trap -
  Computer calculates result to 6 significant figures
  Put these numbers directly in your report
    Average time = 4.53456 s
    implies 4.53456 +/- 0.000005 s
    Obviously ridiculous!
  Accuracy of 1% would be excellent here
    Average time = 4.5 s
    implies 4.5 +/- 0.05 s
  Present a realistic number of significant figures in your report!