## 1. Assembling and Disassembling

1. Convert instruction “addq $t0, $t1, $t2” to binary and hexadecimal.

Answer:

The identifiers t0, t1, t2 are symbolic names for registers 1, 2 and 3 in decimal.

| Field | opcode | regA | regB | Padding | Literal flag | Function | regC |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Hex | 0x10 | 0x01 | 0x02 | 0x0 | 0x0 | 0x20 | 0x3 |
| Binary | 010000 | 00001 | 00010 | 000 | 0 | 0100000 | 00011 |

In binary grouping the bits in lots of 4, we get

0100 0000 0010 0010 0000 0100 0000 0011

In hexadecimal, we get

0x40220403

2. Interpret instruction 0x4e003410 in hexadecimal to assembly instruction format.

Answer:

Writing this in binary, we get

0100 1110 0000 0000 0011 0100 0001 0000

interpret this, we get table

| Field | opcode | regA | Literal value | Literal flag | Function | regC |
| --- | --- | --- | --- | --- | --- | --- |
| Binary | 010011 | 10000 | 00000001 | 1 | 0100000 | 10000 |
| Hex | 0x13 | 0x10 | 0x1 | 0x1 | 0x20 | 0x10 |

So we get the instruction “mulq $16, 1, $16”.

Because the regA and regC are same, so the original instruction may be

“mulq $a0, 1” or “mulq $a0, 1, $a0”.

3. Convert instruction “ldq $t0, -1($t0)” to binary and hexadecimal.

Answer:

The identifier t0 is symbolic name for register 1 in decimal.

| Field | opcode | RegA | regB | displacement |
| --- | --- | --- | --- | --- |
| Hex | 0x29 | 0x01 | 0x01 | 0xffff |
| Binary | 101001 | 00001 | 00001 | 1111 1111 1111 1111 |

In binary grouping the bits in lots of 4, we get

1010 0100 0010 0001 1111 1111 1111 1111

In hexadecimal, we get

0xa421ffff

2. Calculate values in registers after executing a set of instructions

Exercise 1:

# Suppose we have the following values in registers

$t0 0x55

$t1 0x68

$t2 0x24

$t3 0xfffffffffffffff3

How will the registers change after executing the instructions?

(1) subq $t0, 1;

(2) addq $t1, 0x45;

(3) addq $t2, 0x94;

(4) addq $t3, 0x94;

(5) mulq $t1, 0x4;

Answer:

(1) $t0: 0x54

(2) $t1: 0xad

(3) $t2: 0xb8

(4) $t3: 0x87

(5) $t1: 0x2b4

Exercise 2:

Suppose we have the following values in registers

$t0: 0x54

$t1: 0x2b4

$t2: 0xb8

$t3: 0x87

How will the registers change after executing the instructions?

(1) subq $t0, $t1, $t1;

(2) addq $t0, $t1;

(3) subq $t2, 0x124, $t3;

Answer:

(1) $t1: 0xfffffffffffffda0

(2) $t0: 0xfffffffffffffdf4

(3) error: 0x124 is out of range, it can’t be more than 8 bit. You can use instruction like, ldiq, lda, and ldah when the second operand is more than 8 bit.

Exercise 3:

Suppose we have the following values in registers

$t0: 0xfffffffffffffdf4

$t1: 0xfffffffffffffda0

$t2: 0xb8

$t3: 0x87

How will the registers change after executing the instructions?

(1) and $t0, $t1;

(2) bic $t1, 0x55;

(3) bis $t2, $t1, $t1;

(4) eqv $t1, 0x23;

(5) ornot $t3, $t2;

(6) xor $t3, $t1;

Answer:

- $t0: 0xfffffffffffffda0

- $t1: 0xfffffffffffffda0

- $t1: 0xfffffffffffffdb8

- $t1: 0x264

- $t3: 0xffffffffffffffc7

- $t3: 0xfffffffffffffda3

Exercise 4:

Suppose we have the following values in registers

$t0: 0xfffffffffffffda0

$t1: 0x264

$t2: 0xb8

$t3: 0xfffffffffffffda3

How will the registers change after executing the instructions?

- sll $t1,$t3;

- srl $t2,$t2;

- sra $t3,0x4,$t0;

- srl $t3,0x4;

Answer:

- $t1: 0x132000000000

- $t2: 0

- $t0: ffffffffffffffda

- $t3: 0fffffffffffffda

Exercise 5:

Write assembly code to allocate memory for a byte array. The byte array will be used to store asciiz string with max size as 10.

Answer:

abs{

BUFFERSIZE = 10

}

data{

align quad;

buffer:

byte [BUFFERSIZE + 1];

}

3. Memory allocation

Exercise 1:

Draw a memory table to display how following data is stored in memory. Suppose label “value0” refers to memory address 0x000000.

data{

value0:		asciiz	“ab”;

value1:		byte	0x12;

value2:		long	0x3456;

value3:		quad	0x87654321;

}

Answer:

| Address | Label | Content | Address | Label | Content |
| --- | --- | --- | --- | --- | --- |
| 0x000000 | value0 | 0x61 | 0x000008 | value3 | 0x21 |
| 0x000001 |  | 0x62 | 0x000009 |  | 0x43 |
| 0x000002 |  | 0x00 | 0x00000a |  | 0x65 |
| 0x000003 | value1 | 0x12 | 0x00000b |  | 0x87 |
| 0x000004 | value2 | 0x56 | 0x00000c |  | 0x00 |
| 0x000005 |  | 0x34 | 0x00000d |  | 0x00 |
| 0x000006 |  | 0x00 | 0x00000e |  | 0x00 |
| 0x000007 |  | 0x00 | 0x00000f |  | 0x00 |

Exercise 2:

Draw a memory table to display how following data is stored in memory. Suppose label “value0” refers to memory address 0x000000.

data{

align		quad;

value0:		asciiz	“ab”;

align		word;

value1:		byte	0x12;

align 		long;

value2:		word	0x3456;

value3:		long	0x7890;

}

Answer:

| Address | Label | Content | Address | Label | Content |
| --- | --- | --- | --- | --- | --- |
| 0x000000 | value0 | 0x61 | 0x000008 | value2 | 0x56 |
| 0x000001 |  | 0x62 | 0x000009 |  | 0x34 |
| 0x000002 |  | 0x00 | 0x00000a |  | 0x00 |
| 0x000003 |  | 0x00 | 0x00000b |  | 0x00 |
| 0x000004 | value1 | 0x12 | 0x00000c | value3 | 0x90 |
| 0x000005 |  | 0x00 | 0x00000d |  | 0x78 |
| 0x000006 |  | 0x00 | 0x00000e |  | 0x00 |
| 0x000007 |  | 0x00 | 0x00000f |  | 0x00 |